## Slide 1
PnR QoR Report
Design: ssoc_csi2_1p3_cphy_1lane_sys_top
Tool Version: T-2022.03-SP2-1
Report Date: Wed Feb 4 17:11:08 2026
Generated: 2026-03-13 11:20:43

## Slide 2
Executive Summary
Metric | Placement | CTS | Routing
WNS (ns) | -0.172 | -0.786 | -0.623
TNS (ns) | -1.917 | -68.464 | -17.625
Violations | 45 | 244 | 193
DRC Violations | 5 | 16 | 28
Utilization | 0.335 | 0.425 | 0.430

## Slide 3
Placement Stage Details
Timing
Timing QoR: WNS: -0.171638 ns TNS: -1.917389 ns Violating Paths: 45 Worst Group: **in2reg_default**
DRC
Design Rules: Total Nets: 68299 Nets with Violations: 5 Max Trans Violations: 5 Max Cap Violations: 4
Cells
Cell Counts: Leaf Cells: 66047 Combinational: 48574 Sequential: 17473 Buf/Inv: 16153 Macros: 1
Area
Area (um²): Combinational: 52,743.20 Non-combinational: 74,869.53 Macro/Black Box: 471,905.28 Total Cell Area: 599,518.01
Utilization Ratio: 33.50%

## Slide 4
CTS Stage Details
Timing
Timing QoR: WNS: -0.786348 ns TNS: -68.464005 ns Violating Paths: 244 Worst Group: **in2reg_default**
DRC
Design Rules: Total Nets: 88889 Nets with Violations: 16 Max Trans Violations: 10 Max Cap Violations: 5
Cells
Cell Counts: Leaf Cells: 83600 Combinational: 66127 Sequential: 17473 Buf/Inv: 32579 Macros: 1
Area
Area (um²): Combinational: 87,207.51 Non-combinational: 74,908.45 Macro/Black Box: 471,905.28 Total Cell Area: 634,021.24
Utilization Ratio: 42.55%

## Slide 5
Routing Stage Details
Timing
Timing QoR: WNS: -0.622696 ns TNS: -17.624776999999998 ns Violating Paths: 193 Worst Group: cphy_internal_rx_word_clk_mux
DRC
Design Rules: Total Nets: 89861 Nets with Violations: 28 Max Trans Violations: 19 Max Cap Violations: 4
Cells
Cell Counts: Leaf Cells: 84572 Combinational: 67099 Sequential: 17473 Buf/Inv: 33551 Macros: 1
Area
Area (um²): Combinational: 88,887.04 Non-combinational: 74,920.55 Macro/Black Box: 471,905.28 Total Cell Area: 635,712.87
Utilization Ratio: 43.00%

## Slide 6
Stage-wise Comparison
Stage | WNS (ns) | TNS (ns) | Violations
Placement | -0.171638 | -1.917389 | 45
CTS | -0.786348 | -68.464005 | 244
Routing | -0.622696 | -17.624776999999998 | 193
Notes:
- WNS (Worst Negative Slack): Negative values indicate timing violations
- TNS (Total Negative Slack): Sum of all negative slacks
- Green = Pass (positive slack), Red = Fail (negative slack)